## Slide 1: P&S Modern SSDs Address Mapping & Garbage Collection
Dr. Mohammad Sadrosadati
Prof. Onur Mutlu
ETH Zürich
Fall 2022
23 November 2022

## Slide 2: Recap: SSD & NAND Flash Memory
SSD organization
  SSD controller: Multicore CPU + per-channel flash controllers
  DRAM: Metadata store, 0.1% of SSD capacity
  NAND flash chips
    Channel (Package(s)) – Die – Plane – Block – Page
NAND flash characteristics
  Erase-before-write, asymmetry in operation units (read/program: page, erase: block), limited endurance, retention loss…
Basic NAND flash opeartions
  Read/program/erase

## Slide 3: Recap: Advanced Commands
Subpage Sensing & Random Data Out (RDO)
  For I/O-unit mismatch b/w OS and NAND flash memory
Cache Read Command
  For improving a chip’s read throughput
  By overlapping data transfer and page sensing
Multi-Plane Operations
  For improving a chip’s throughput
  By enabling concurrently operation of multiple planes
Program & Erase Suspensions
  For improving the read latency (operation latency asymmetry)
  By prioritizing latency-sensitive reads over writes/erases

## Slide 4: Today’s Agenda
Advanced NAND Flash Commands
Address Translation & Garbage Collection

## Slide 5: Flash Translation Layer: Overview
SSD firmware (often referred to as SSD controller)
  Provides backward compatibility with traditional HDDs
  By hiding unique characteristics of NAND flash memory
Responsible for many important SSD-management tasks
  Address translation + garbage collection
    Performs out-of-place writes due to erase-before-write property
  Wear leveling
    To prolong SSD lifetime by evenly distributing P/E cycles
  Data refresh
    Resets transient errors by copying data to a new page(s)
  I/O scheduling
    To take full advantage of SSD internal parallelism

## Slide 6: Flash Translation Layer: Overview
SSD firmware (often referred to as SSD controller)
  Provides backward compatibility with traditional HDDs
  By hiding unique characteristics of NAND flash memory
Responsible for many important SSD-management tasks
  Address translation + garbage collection
    Performs out-of-place writes due to erase-before-write property
  Wear leveling
    To prolong SSD lifetime by evenly distributing P/E cycles
  Data refresh
    Resets transient errors by copying data to a new page(s)
  I/O scheduling
    To take full advantage of SSD internal parallelism

## Slide 7: Simple SSD Architecture
NAND Flash Chip (Single Plane)
Flash Translation Layer
Page
Block0
Block1
Block2
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Storage view at the operating-system level: A flat block device
LBA
Logical Block Address

## Slide 8: Simple SSD Architecture
NAND Flash Chip (Single Plane)
Flash Translation Layer
Page
Block0
Block1
Block2
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
PPA
Phygical Page Address
PBA
Phygical Block Address
LBA
Logical Block Address
Overprovisioning:
Physical capacity > Logical capaciy
For performance & lifetime

## Slide 9: Write Request Handling: Page Write
NAND Flash Chip (Single Plane)
Flash Translation Layer
Block0
Block1
Block2
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19

## Slide 10: Write Request Handling: Page Write
NAND Flash Chip (Single Plane)
Flash Translation Layer
Block0
Block1
Block2
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 0, Size: 1, DIR: W, A)

## Slide 11: Write Request Handling: Page Write
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
Block0
Block1
Block2
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 0, Size: 1, DIR: W, A)

## Slide 12: Write Request Handling: Page Write
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
Block0
Block1
Block2
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 0, Size: 1, DIR: W, A)
Note:
We are asumming that logical block size = physical page size
LB size = 4 KiB, PP size = 16 KiB

## Slide 13: Write Request Handling: Sequential Write
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
Block0
Block1
Block2
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19

## Slide 14: Write Request Handling: Sequential Write
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
Block0
Block1
Block2
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Sequential (large) write
Req (LBA: 4, Size: 12, DIR: W, B … M)

## Slide 15: Write Request Handling: Sequential Write
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Sequential (large) write
PROG(PPA: 1, B)
PROG(PPA: 2, C)
PROG(PPA: 12, M)
…
12 page-program commands
Req (LBA: 4, Size: 12, DIR: W, B … M)

## Slide 16: Write Request Handling: Sequential Write
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Sequential (large) write
PROG(PPA: 1, B)
PROG(PPA: 2, C)
PROG(PPA: 12, M)
…
12 page-program commands
Req (LBA: 4, Size: 12, DIR: W, B … M)
Active block (or write-point) approach
  Keep only one block being written
  Due to the open-block problem
Program-sequence constraint
  Fixed program order within a block
  Due to cell-to-cell interference

## Slide 17: Write Request Handling: Address Mapping
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Problem: LBA (or LPA) does not match PPA!

## Slide 18: Write Request Handling: Address Mapping
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Problem: LBA (or LPA) does not match PPA!
Req (LBA: 4, Size: 1, DIR: R)
READ (PPA: ?)
Needs to maintain
Address-mapping information

## Slide 19: Write Request Handling: Address Mapping
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 4, Size: 1, DIR: R)
READ (PPA: ?)
LPA | PPA
0 | 0
… | …
4 | 1
5 | 2
… | …
Mapping Table

## Slide 20: Write Request Handling: Address Mapping
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 4, Size: 1, DIR: R)
READ (PPA: 1)
LPA | PPA
0 | 0
… | …
4 | 1
5 | 2
… | …
Mapping Table

## Slide 21: Write Request Handling: Update
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 0
… | …
4 | 1
5 | 2
… | …
Mapping Table

## Slide 22: Write Request Handling: Update
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 0, Size: 1, DIR: W, A’)
LPA | PPA
0 | 0
… | …
4 | 1
5 | 2
… | …
Mapping Table

## Slide 23: Write Request Handling: Update
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 0, Size: 1, DIR: W, A’)
PROG (PPA: 13,A’)
LPA | PPA
0 | 0
… | …
4 | 1
5 | 2
… | …
Mapping Table

## Slide 24: Write Request Handling: Update
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 0, Size: 1, DIR: W, A’)
PROG (PPA: 13,A’)
LPA | PPA
0 | 13
… | …
4 | 1
5 | 2
… | …
Mapping Table
Invalid
Update Mapping

## Slide 25: Write Request Handling: Update
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
A’
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 0, Size: 1, DIR: W, A’)
PROG (PPA: 14,A’)
LPA | PPA
0 | 14
… | …
4 | 1
5 | 2
… | …
Mapping Table

## Slide 26: Write Request Handling: Update
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
A’
A’
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 0, Size: 1, DIR: W, A’)
PROG (PPA: 15,A’)
LPA | PPA
0 | 15
… | …
4 | 1
5 | 2
… | …
Mapping Table

## Slide 27: Write Request Handling: Update
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
A’
A’
Block3
A’
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 0, Size: 1, DIR: W, A’)
PROG (PPA: 16,A’)
LPA | PPA
0 | 16
… | …
4 | 1
5 | 2
… | …
Mapping Table
Running
out of free pages

## Slide 28: Garbage Collection
Reclaims free pages by erasing invalid pages
  Erase unit: block
  If a victim block (to erase) has valid pages, all the valid pages need to be copied to other free pages
    Performance overhead: (tREAD + tPROG)×# of valid pages
    Lifetime overhead: additional writes  P/E-cycle increase
Greedy victim-selection policy: Erases the block with the largest number of invalid pages
  Needs to maintain # of invalid (or valid) pages for each block

## Slide 29: Write Request Handling: Garbage Collection
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
A’
A’
Block3
A’
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 16
… | …
4 | 1
5 | 2
… | …
Mapping Table
PBA | Status
0 | IVVV
1 | VVVV
2 | VVVV
3 | VIII
4 | VFFF
Status Table
F: free, V: valid, I: invalid
READ (PPA: 12)

## Slide 30: Write Request Handling: Garbage Collection
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
A’
A’
Block3
A’
M
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 16
… | …
4 | 1
5 | 2
… | …
Mapping Table
PBA | Status
0 | IVVV
1 | VVVV
2 | VVVV
3 | VIII
4 | VFFF
Status Table
F: free, V: valid, I: invalid
READ (PPA: 12)
PROG (PPA: 17, M)

## Slide 31: Write Request Handling: Garbage Collection
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
A’
A’
Block3
A’
M
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 16
… | …
4 | 1
5 | 2
… | …
Mapping Table
PBA | Status
0 | IVVV
1 | VVVV
2 | VVVV
3 | IIII
4 | VVFF
Status Table
F: free, V: valid, I: invalid
READ (PPA: 12)
PROG (PPA: 17, M)
Update Status

## Slide 32: Write Request Handling: Garbage Collection
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
A’
A’
Block3
A’
M
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 16
… | …
4 | 1
… | …
15 | 12
Mapping Table
PBA | Status
0 | IVVV
1 | VVVV
2 | VVVV
3 | IIII
4 | VVFF
Status Table
F: free, V: valid, I: invalid
READ (PPA: 12)
PROG (PPA: 17, M)
Update Status
Update Mapping

## Slide 33: Write Request Handling: Garbage Collection
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
A’
A’
Block3
A’
M
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 16
… | …
4 | 1
… | …
15 | 17
Mapping Table
PBA | Status
0 | IVVV
1 | VVVV
2 | VVVV
3 | IIII
4 | VVFF
Status Table
F: free, V: valid, I: invalid
READ (PPA: 12)
PROG (PPA: 17, M)
Update Status
Update Mapping

## Slide 34: Write Request Handling: Garbage Collection
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
A’
A’
Block3
A’
M
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 16
… | …
4 | 1
… | …
15 | 17
Mapping Table
PBA | Status
0 | IVVV
1 | VVVV
2 | VVVV
3 | IIII
4 | VVFF
Status Table
F: free, V: valid, I: invalid
READ (PPA: 12)
PROG (PPA: 17, M)
Update Status
Update Mapping
Q: How FTL knows PPA 12 (data M) is mapped to LPA 15?
  Unless it maintains P2L mappings?
A: P2L mapping is stored in each physical page’s OOB (Out-of-Band) area

## Slide 35: Write Request Handling: Garbage Collection
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
Block3
A’
M
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 16
… | …
4 | 1
… | …
15 | 17
Mapping Table
PBA | Status
0 | IVVV
1 | VVVV
2 | VVVV
3 | IIII
4 | VVFF
Status Table
F: free, V: valid, I: invalid
READ (PPA: 12)
PROG (PPA: 17, M)
BERS (PBA: 3)

## Slide 36: Write Request Handling: Garbage Collection
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
Block3
A’
M
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 16
… | …
4 | 1
… | …
15 | 17
Mapping Table
PBA | Status
0 | IVVV
1 | VVVV
2 | VVVV
3 | FFFF
4 | VVFF
Status Table
F: free, V: valid, I: invalid
READ (PPA: 12)
PROG (PPA: 17, M)
BERS (PBA: 3)
Update Status

## Slide 37: Write Request Handling: Garbage Collection
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
Block3
A’
M
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 16
… | …
4 | 1
… | …
15 | 17
Mapping Table
PBA | Status
0 | IVVV
1 | VVVV
2 | VVVV
3 | FFFF
4 | VVFF
Status Table
F: free, V: valid, I: invalid
READ (PPA: 12)
PROG (PPA: 17, M)
BERS (PBA: 3)
Update Status
Note:
Block erasure (and status update) is done just before programming a new page to the block (i.e., lazy erase)
  Due to the open-block problem

## Slide 38: Performance Issues
Garbage collection significantly affects SSD performance
  High latency: Large block size of modern NAND flash memory
    Assume 1) a block contains 576 pages, 2) only 5% of the pages in the victim block are valid 3) tR = 100 us, tPROG = 700 us, tBERS = 5 ms
      # of pages to copy = 576×0.05 = 28.8  28 pages
      GC latency > 28×(tR + tPROG) + tBERS = 27,400 us
    Order(s) of magnitude larger latency than tR and tPROG
    Copy operations are the major contributor (rather than tBERS)
  If FTL performs GC in an atomic manner, it delays user requests for a significantly long time
    Long tail latency (performance fluctuation)
    Noisy neighbor: a read-dominant workload’s performance would be significantly affected when running with a write-intensive workload (+ performance fairness problem)

## Slide 39: Performance Issues: Mitigation
TRIM (UNMAP or discard) command
  Informs FTL of deletion/deallocation of a logical block
  Allows FTL to skip copy of obsolete (i.e., invalid) data
Background GC: Exploits SSD idle time
  Challenge: how to accurately predict SSD idle time
  Premature GC: copied pages could have been invalidated by the host system
Progressive GC: Divide GC process into subtasks
  e.g., copying 28 pages  (copying 1 page + servicing user request)×28
  Effective at decreasing tail latency

## Slide 40: Required Materials
Address Mapping
  Aayush Gupta, Yongjae Kim, and Bhuvan Urgaonkar, “DFTL: A Flash Translation Layer Employing Demand-based Selective Caching of Page-level Address Mappings,” In ASPLOS 2009.

## Slide 41: Recommend Materials
Cache read & Read-retry
  Jisung Park, Myungsuk Kim, Lois Orosa, Jihong Kim, and Onur Mutlu, “Reducing Solid-State Drive Read Latency by Optimizing Read-Retry,” In ASPLOS 2021.
Program & Erase Suspension
  Guanying Wu and Xunbin He, “Reducing SSD Read Latency via NAND Flash Program and Erase Suspension,” In USENIX FAST 2012.
  Shine Kim, Jonghyun Bae, Hakbeom Jand, Wenjing Jin, Jeonghun Gong, Seungyeon Lee, Tae Jun Ham, and Jae W. Lee, “Practical Erase Suspension for Modern Low-latency SSDs,” In USENIX ATC 2019.

## Slide 42: P&S Modern SSDs Address Mapping & Garbage Collection
Dr. Mohammad Sadrosadati
Prof. Onur Mutlu
ETH Zürich
Fall 2022
23 November 2022